## Slide 1: Magnetic Resonance Imaging: how does it work?
Philippe Karan
Université de Sherbrooke
SCIL

## Slide 2: Towards understanding MRI
Physics
  Magnetic field and induction
  Spin and precession
  Magnetization
  Resonance
Principles of magnetic resonance imaging
  Signal
  Relaxation
  Sequences
Image formation
  Slice selection
  Spatial encoding
Diffusion MRI
Magnetization transfer

## Slide 3: Physics: magnetic field
gravitational
electromagnetic
weak
strong
Fundamental forces
of the Universe
mathematical
representation
Fields
of interactions
Notes: A field is not made of anything in particular; it is just a region of space in which a force acts. The type of force determines what is influenced by the force in the field (e.g., in an electric field, the force will act on a charge).

## Slide 4: Physics: magnetic field
Electric field
Magnetic field
Electromagnetic field
Magnetic charge?
or
Varying electric field
Magnetic dipole
or
Varying electric field
Maxwell’s equations!
Electric charge
or
Varying magnetic field
N
S
Induction
Spin

## Slide 5: Physics: spin
Angular momentum: momentum from rotation
Classical mecanics
Property, like mass or charge
Quantum mecanics
Spin: intrinsic angular momentum
particles
Electrons, protons, neutrons, have spin 1/2
When , only two eigenstates: "up" or "down"
Quantized
N
S
Intrinsic magnetic dipole
B
Notes: Particles with spin have an intrinsic magnetic moment proportionnal to their spin : mu = g q S / 2m.
Spin « one half »
The spins « tend » to align with B0

## Slide 6: Physics: precession
Classical mecanics
Spins around its axis of rotation AND
around the direction of the gravitational field
Precession
Quantum mecanics
g
B
The magnetic moment precesses around
the external magnetic field
Precise angular frequency: Larmor frequency
Notes: This precession is assuming a positive gyromagnetic ratio (as for protons or electrons)

## Slide 7: Physics: spin and precession
But wait!
We said: only two eigenstates: "up" or "down"
And now: the magnetic dipole precesses around the magnetic field
B
B
Which one is it?
Notes: This precession is assuming a positive gyromagnetic ratio (as for protons or electrons)

## Slide 8: Physics: spin and precession
= a
+ b
Superposition of the two principal states
Thanks quantum physics!
Precesses
When measured: only two states possible
For simplicity: we tend to talk about spins as either up or down,
but don’t forget about the superposition and precession!
Notes: This precession is assuming a positive gyromagnetic ratio (as for protons or electrons)

## Slide 9: Physics: magnetization
What about an ensemble of spins?
No macroscopic
magnetic moment
Net magnetization
Net magnetization
increases with B
up: lower energy
down: higher energy
M
M
B0
B0
B0
Notes: The gap between energy levels increases with B and 1/T.
This is an exageration, as in reality, the amount of spins not cancelling out is about a few ppm. So the NMR signal is very weak.
We are gonna love magnetization for now on, because it will enable us to understand MRI without talking much about spins!

## Slide 10: Physics: magnetization
Does the magnetization also precesses?
No
transverse magnetization
B0
Not in phase
(not synchronized)
B0
0
Mz
Mxy
No
longitudinal
magnetization
Mz
Mxy
Spins contributing to Mxy : in phase coherence
(synchronized)
90° rotation
Static!
Precesses!

## Slide 11: Physics: resonance
Remember induction?
Varying magnetic field
Induced electric current
Exciting it the proper way
Signal!
M
Needs to move
Push at the right beat
Maximum energy absorption
Resonant frequency
Notes: Excite = give it energy
Analogie de la balançoire: pour la pousser plus haut
(donner de l’énergie), il faut pousser à la même fréquence
que le balan, sinon on brise l’élan. Même chose avec le spin,
pour l’exciter (lui donner de l’énergie), il faut le « pousser » à
sa fréquence « de résonance », qui est la fréquence de Larmor
dans ce cas-ci!
Ça prend de l’énergie pour être perpendiculaire au champ B0!

## Slide 12: Physics: resonance
Remember induction?
Varying magnetic field
Induced electric current
Exciting it the proper way
Signal!
M
Needs to move
Larmor frequency
Resonant frequency
B
"Push" it at the
Notes: Excite = give it energy
Analogie de la balançoire: pour la pousser plus haut
(donner de l’énergie), il faut pousser à la même fréquence
que le balan, sinon on brise l’élan. Même chose avec le spin,
pour l’exciter (lui donner de l’énergie), il faut le « pousser » à
sa fréquence « de résonance », qui est la fréquence de Larmor
dans ce cas-ci!
Ça prend de l’énergie pour être perpendiculaire au champ B0!

## Slide 13: Towards understanding MRI
Physics
  Magnetic field and induction
  Spin and precession
  Magnetization
  Resonance
Principles of magnetic resonance imaging
  Signal
  Relaxation
  Sequences
Image formation
  Slice selection
  Spatial encoding
Diffusion MRI
Magnetization transfer

## Slide 14: Principles of MRI: name
Excited at
Larmor frequency
Magnetic Resonance Imaging
Spins and
magnetization
Resonance
phenomena
Making an
image
Nuclear
From the
nucleus
O
H
H
Water
Hydrogen nucleus
Proton: spin 1/2
B
tons
M
Measured
via
induction
Notes: Making an image from the nucleus’ spin / the nuclei’s magnetization, using the resonance phenomena.

## Slide 15: Principles of MRI: sequences
Frequency encoding
Signal
Phase encoding
Slice selection
RF pulses
Pre-pulse
90° RF pulse
180° RF pulse
Spin echo
Gz
Gy
Gx
What we know so far:

## Slide 16: Principles of MRI: signal
B0
M
z
y
x
B0
M
Radio
frequency (RF)
pulse
Deflects out of equilibrium
Precesses around B0
Larmor frequency
Notes: Free induction decay

## Slide 17: Principles of MRI: signal
M
z
y
x
B0
M
z
y
x
B0
M
z
y
x
B0
M
z
y
x
B0
Precessing while tilting: spiral-like trajectory
Notes: Free induction decay

## Slide 18: Principles of MRI: signal
M
z
y'
x'
B0
B1
Rotating frame of reference
RF pulse
=
Magnetic field B1 applied for a short time
M precesses around B1
RF flip angle
M
z
y
x
B0
RF pulse
Notes: Free induction decay

## Slide 19: Principles of MRI: signal
Mz = M
z
y
x
B0
M
z
y
x
B0
M
z
y
x
B0
Only Mxy is detected via induction
Mxy = 0
Mz
Mxy
M
Flip angle of 90°
=
maximum MR signal
Mz = 0
Mxy = M
90° RF pulse
Transverse component
Longitudinal component
Notes: Free induction decay

## Slide 20: Principles of MRI: signal
What about individual spins?
Random
precession
RF pulse
coherent precession of the spins
Transverse magnetization Mxy
Coherent
precession
RF pulse
Notes: After the RF pulse, the spins all precesse around B0 in a synchronized way, not cancelling each other out!

## Slide 21: Principles of MRI: signal
Quick summary
z
y
x
B0
M
M
z
y
x
B0
Magnetic field B0 generates a net magnetization M
Radio frequency
pulse flips M by an angle
Magnetization M starts precessing around B0
Rotating magnetic field induces a signal

## Slide 22: Principles of MRI: sequences
Frequency encoding
Signal
Phase encoding
Slice selection
RF pulses
Pre-pulse
90° RF pulse
180° RF pulse
Gz
Gy
Gx
What we know so far:
90° RF pulse flips the magnetization
Spin echo

## Slide 23: Principles of MRI: signal
Quick summary
How does this produce tissue contrast?
z
y
x
B0
M
M
z
y
x
B0
Magnetic field B0 generates a net magnetization M
Radio frequency
pulse flips M by an angle
Magnetization M starts precessing around B0
Rotating magnetic field induces a signal

## Slide 24: Principles of MRI: relaxation
M
z
y
x
B0
Why is the signal diminishing?
Relaxation
y
x
Time
Signal amplitude
The rate of relaxation depends of the tissue
FID
Free Induction Decay

## Slide 25: Principles of MRI: relaxation
What is relaxation?
The process of Mz and Mxy returning to their equilibrium values
M
0
Mxy disappears
Mz is restored
Different processes
Mxy
Mz

## Slide 26: Principles of MRI: relaxation
Longitudinal relaxation
Spin-lattice relaxation
After RF pulse: excited nuclei
Higher energy
Spin up: nuclei at equilibrium
Lower energy
Excited nuclei
Interact with the lattice
Mz is restored
Back to equilibrium
Transfer energy
External environment

## Slide 27: Principles of MRI: relaxation
Longitudinal relaxation
Lattice fields: magnetic fields created by surrounding nuclei
How is energy
transfered?
Must fluctuate at the Larmor frequency
Interacting
Also true for
relaxation!

## Slide 28: Principles of MRI: relaxation
Longitudinal relaxation
Lattice fields: magnetic fields created by surrounding nuclei
Must fluctuate at the Larmor frequency
Molecular motion: rotation, vibration, translation
Fluctuations
of lattice fields
Various frequency, or "speed"
From random thermal activity
Size of molecules
Physical state
Macromolecules
Notes: Don’t forget that these lattice fields are LOCAL, and thus, don’t affect all spins the same way, creating contrast!

## Slide 29: Principles of MRI: relaxation
Longitudinal relaxation
Simplistic description
Larmor frequency
Low frequency
High frequency
Large
Size of molecules
Medium
Small
Physical state
Solids
Solutions
Pure liquids
Macromolecules
O
H
H
Macromolecule
O
H
H
Hydration layers
Bound water
Structured water
Slows motion: faster relaxation
Pathologies
Notes: Don’t forget that these lattice fields are LOCAL, and thus, don’t affect all spins the same way, creating contrast!
Solids : high vibrational frequency
Pure liquids : high translational frequency

## Slide 30: Principles of MRI: relaxation
Chart: 
Time
Mz
Initial M
0
63%
T1
Longitudinal relaxation
Characteristic relaxation time T1
Exponential fashion
Shorter T1 = faster relaxation
Longer T1 = slower relaxation
T1 relaxation

## Slide 31: Principles of MRI: relaxation
Longitudinal relaxation
Larmor frequency
Low frequency
High frequency
Large
Size of molecules
Medium
Small
Physical state
Solids
Solutions
Pure liquids
Macromolecules
O
H
H
Macromolecule
O
H
H
Hydration layers
Bound water
Structured water
Slows motion: faster relaxation
Pathologies
Short T1
Long T1
Long T1
Shorter T1
Longer T1
Notes: Don’t forget that these lattice fields are LOCAL, and thus, don’t affect all spins the same way, creating contrast!
Solids : high vibrational frequency
Pure liquids : high translational frequency

## Slide 32: Principles of MRI: relaxation
Longitudinal relaxation
Lattice fields are local
T1 values vary around the body
By measuring T1, we can see different tissues!
T1
Liver
Kidney
Fat
Gray matter
White matter
Cerebrospinal fluid
Lung
Skeletal muscle
250 ms
4000 ms

## Slide 33: Principles of MRI: relaxation
Transverse relaxation
Mxy disappears
Spin-spin relaxation
Before RF pulse: random precession of the spins
Mxy
After RF pulse: coherent precession of the spins
Mxy
not in phase
in phase
Coherent precession
Random precession
T1 relaxation
Spin-spin interaction
Notes: Important to note that tipping the net magnetization (M) into the transverse plane does not cause all the spins to magically lock in phase. What happens is that those same spins initially showing some statistical "preference" for the z-direction prior to the RF-pulse have now been rotated into the transverse plane. The initial Boltzmann distribution "ordering" of spins in the z-direction has been preserved and transformed by the rotation into what can be considered "phase coherence" in the xy-plane. Simultaneously, the initial value of M in the z-direction (Mz) immediately before the RF-pulse has been converted to a net transverse magnetization (Mxy) after the pulse.
The presence of a non-zero net transverse magnetization (Mxy) is at any time is evidence of persistent asymmetry of transverse components of angular momentum, and what is commonly called "phase coherence." Any process that disrupts either the number or relative positions of these transverse components will result in T2 relaxation.

## Slide 34: Principles of MRI: relaxation
Transverse relaxation
T1 relaxation: spins transfering their excess energy
Gain of Mz Loss of Mxy
Any process causing longitudinal relaxation also results in transverse relaxation!
Spin-spin interaction: transverse relaxation without longitudinal relaxation

## Slide 35: Principles of MRI: relaxation
Transverse relaxation
Interactions
between spins
Local magnetic
field variations
Gradual and seemingly random dephasing
Decay of Mxy
Mxy
z
y
x
z
y
x
z
y
x
z
y
x
Time
Individual nuclei start precessing at slightly different frequencies
Feel a different magnetic field!
Notes: Interactions between spins, but also the presence of charges in mouvement, atoms with non-zero nuclear spins or atoms with superparamagnetic properties, cause the local magnetic fields to vary.

## Slide 36: Principles of MRI: relaxation
Chart: 
Time
Mxy
M after RF
0
37%
T2
Characteristic relaxation time T2
Exponential fashion
Mxy
z
y
x
z
y
x
z
y
x
z
y
x
Time
T2 relaxation

## Slide 37: Principles of MRI: relaxation
Transverse relaxation
Solids and large molecules: fixed structure maintains the magnetic field
Pure liquids and small molecules: rapid translational motion averages the local magnetic field variations
Macromolecules and bound water: reduces the overall molecular motion
Short T2
Long T2
Shorter T2
* T2 time is independent of magnefield field strength

## Slide 38: Principles of MRI: relaxation
Transverse relaxation
T2 values vary around the body
By measuring T2, we can see different tissues!
T2
Liver
Kidney
Fat
Gray matter
White matter
Cerebrospinal fluid
Lung
Skeletal muscle
Local magnetic
field variations
T1
Liver
Kidney
Fat
Gray matter
White matter
Cerebrospinal fluid
Lung
Skeletal muscle
x10
250 ms
4000 ms
2000 ms
40 ms

## Slide 39: Principles of MRI: relaxation
Chart: 
Time
Mz
0
63%
T1
Longitudinal relaxation
Chart: 
Time
Mxy
M after RF
0
37%
T2
Initial M
Transverse relaxation
T2 relaxation
What we measure
directly
T1 relaxation
We can’t measure
directly
***

## Slide 40: Principles of MRI: relaxation
T2 relaxation
*

## Slide 41: Principles of MRI: relaxation
Inhomogeneities in the applied magnetic field B0
Reduce spin coherence
T2 relaxation + field inhomogeneities = effective transverse relaxation
T2*
Time
Signal amplitude
T2 decay
T2* decay
Naive measurement:
T2* relaxation
How do we measure
T2 relaxation?

## Slide 42: Principles of MRI: spin echo
T2 relaxation
Field inhomogeneities
fundamentally
different
random
irreversible
static influence
"reversible"
Mxy
z
y
x
z
y
x
z
y
x
z
y
x
Time

## Slide 43: Principles of MRI: spin echo
Analogy: Runners on a circular track with wind
Different abilities
of runners
Inhomogeneities in
the magnetic field
Random influence
of the wind
Random spin-spin
interactions
No static influence
Only random influence
In phase
Dephasing
Turn around!

## Slide 44: Principles of MRI: spin echo
Mxy
z
y
x
z
y
x
z
y
x
z
y
x
Time
z
y
x
z
y
x
z
y
x
z
y
x
slowest
fastest
slowest
fastest
After
90° pulse
180° RF
pulse
After
180° pulse
Turn around!
Mxy
Spin echo
Dephasing
Rephasing

## Slide 45: Principles of MRI: spin echo
Echo signal amplitude smaller than original FID
Spin-spin interactions
(wind) are not reversible
T2 relaxation
Signal amplitude
T2 decay
T2* decay
FID
2nd echo
Time
90° RF
pulse
180° RF
pulse
TE
TE/2
1st echo
180° RF
pulse
TE: echo time
Notes: Measuring spin echo signal, instead of the FID, permits more complete evolution of spin-spin interactions while offering a vehicle for correcting the influence of static field inhomogeneities.

## Slide 46: Principles of MRI: sequences
Frequency encoding
Signal
Phase encoding
Slice selection
RF pulses
Pre-pulse
90° RF pulse
180° RF pulse
Gz
Gy
Gx
What we know so far:
90° RF pulse flips the magnetization
90 ° and 180° RF pulses create a spin echo
Spin echo

## Slide 47: Principles of MRI: inversion
What about measuring
T1 relaxation?
Time
Mz
0
Short T1
M initial
-M initial
180° RF pre-pulse
90° RF pulse
Long T1
TI
Chart: 
Many tricks
Inversion recovery
Suppression of tissues

## Slide 48: Principles of MRI: timing
Short TE
T1 and T2 short
T1 and T2 long
Combination of short TE and short TR gives T1 contrast.
As opposed to typical long TR and "long" TE giving T2 contrast.
RF pulses

## Slide 49: Principles of MRI: sequences
Frequency encoding
Signal
Phase encoding
Slice selection
RF pulses
Pre-pulse
90° RF pulse
180° RF pulse
Gz
Gy
Gx
What we know so far:
90° RF pulse flips the magnetization
90 ° and 180° RF pulses create a spin echo
Pre-pulse prepares the spins for contrast
Spin echo

## Slide 50: Towards understanding MRI
Physics
  Magnetic field and induction
  Spin and precession
  Magnetization
  Resonance
Principles of magnetic resonance imaging
  Signal
  Relaxation
  Sequences
Image formation
  Slice selection
  Spatial encoding
Diffusion MRI
Magnetization transfer

## Slide 51: Image formation
Larmor frequency
1.
2.
3.
4.
Whole head
resonates at the same frequency*
No spatial information!

## Slide 52: Image formation
Solution: encode the spatial position of the nuclei into the signal
Spatial encoding of the signal coming from that slice
Selection of an image slice
Larmor frequency
Function of the strength of B0
Make it a function of position
Magnetic field gradient

## Slide 53: Image formation: slices
z
B0
Gz
RF frequency
One single
Larmor frequency
Multiple
Larmor frequencies
Magnetic field gradient
Slice thickness
Bandwidth
Gradient amplitude
Slice thickness
Bandwidth
Gradient amplitude
RF pulse

## Slide 54: Image formation: slices
z
B0
Gz
RF frequency
Spin phase
z
B0
Gz
RF frequency
Spin phase
Slice selection gradient
Spin rephasing gradient
Dephasing:
Spiral staircase
Maximum
signal

## Slide 55: Principles of MRI: sequences
Frequency encoding
Signal
Phase encoding
Slice selection
RF pulses
Pre-pulse
90° RF pulse
180° RF pulse
Gz
Gy
Gx
Spin echo
What we know so far:
90° RF pulse flips the magnetization
90 ° and 180° RF pulses create a spin echo
Pre-pulse prepares the spins for contrast
Gradients Gz select a single slice

## Slide 56: Image formation: encodings
Gx
Dephasing along Gx
No dephasing
Larmor frequency,
y
x
z
Notes: Tout au long de l’application du gradient G_x, le niveau de déphasage augmente (de façon périodique, en passant parfois par des rephasages). Donc durant G_x on parcourt la ligne k_x.

## Slide 57: Image formation: encodings
or
Gx
Gx
Gx
Gx
x
0°
360°
kx
Chart: 
x
0°
720°
kx
Chart: 
360°
x
0°
360°
720°
1080°
kx
Chart: 
x
Dephasing
Spatial frequency
No gradient
No dephasing
Phase
Amount of dephasing
Inverse Fourier Transform
Gx
MRI signal
Notes: Tout au long de l’application du gradient G_x, le niveau de déphasage augmente (de façon périodique, en passant parfois par des rephasages). Donc durant G_x on parcourt la ligne k_x.

## Slide 58: Image formation: encodings
Spatial encoding with the phase encoding gradient Gy.
Gy
+
++
0
0
0
0
0
0
0
0
0
0
++
++
++
+
+
+
0
0
0
y
x
z
Time
0
0
0
0
0
0
0
0
0
Phase memory!
Single value of ky:
Same
frequency
Different
phases
Single gradient
Gy
Notes: Tout au long de l’application du gradient G_x, le niveau de déphasage augmente (de façon périodique, en passant parfois par des rephasages). Donc durant G_x on parcourt la ligne k_x.

## Slide 59: Image formation: encodings
Spatial encoding with the frequency encoding gradient Gx.
Gx
+
++
0
Gx
+
++
0
Gx
+
++
0
y
x
z
Time
0
0
0
0
0
0
0
0
0
0
+
++
0
+
++
0
+
++
0
+
++
0
+
++
0
+
++
0
+
++
0
+
++
0
+
++
Gx
Gx
Gx
Gy
kx=0, ky
kx= Gxt1, ky
kx= Gxt2, ky
kx= Gxt3, ky
1
2
3
Notes: Tout au long de l’application du gradient G_x, le niveau de déphasage augmente (de façon périodique, en passant parfois par des rephasages). Donc durant G_x on parcourt la ligne k_x.

## Slide 60: Image formation: encodings
Spatial encoding of the signal from a slice, in both axis.
Image
Inverse
2D FT
Points in
k-space
…
Nx points
Ny lines
ky
kx
Chart: 
Ny gradients Gy
One gradient Gx,
Nx data points
Chart: 
Chart: 
…
Frequency encoding
Phase encoding
Gy
Gx
S(kx, ky)
kx
Measurement
Ny gradients
Nx points
ky

## Slide 61: Principles of MRI: sequences
Frequency encoding
Signal
Phase encoding
Slice selection
RF pulses
Pre-pulse
90° RF pulse
180° RF pulse
Gz
Gy
Gx
Spin echo
What we know so far:
90° RF pulse flips the magnetization
90 ° and 180° RF pulses create a spin echo
Pre-pulse prepares the spins for contrast
Gradients Gz select a single slice in z-axis
Gradients Gy encode the y-axis
Gradients Gx encode the x-axis and read

## Slide 62: Principles of MRI: sequences
Frequency encoding
Signal
Phase encoding
Slice selection
RF pulses
Pre-pulse
90° RF pulse
180° RF pulse
Gz
Gy
Gx
Spin echo
1
2
3
4
i
ii
ky
kx
kx
1
2
3
4
Sequence with Gy version i
Sequence with Gy version ii
ky
i
i
ii

## Slide 63: Towards understanding MRI
Physics
  Magnetic field and induction
  Spin and precession
  Magnetization
  Resonance
Principles of magnetic resonance imaging
  Signal
  Relaxation
  Sequences
Image formation
  Slice selection
  Spatial encoding
Diffusion MRI
Magnetization transfer

## Slide 64: Diffusion: principles
What is diffusion?
Brown
[1828]
Einstein
[1905]
"Random microscopic movement of particles or small molecules due to thermal agitation."
Diffusion propagator
Random walk in isotropic and homogeneous medium
Mean squared displacement
Diffusion coefficient
Linear relation broken when medium is constrained!
Time dependent
ADC
Apparent
diffusion coefficient
Different ADC!
Notes: Note pour présentation physique IRM : La façon la plus simple de faire un encodage "sphérique" c'est en mettant back à back trois gradients linéaires perpendiculaires. C'est évidemment pas optimal pcq ça capture pas toutes les directions, donc on prend plutôt un gradient qui se promène dans le temps et qui encode bien la sphère. Pour le planaire, même chose, on pourrait voir ça comme la combinaison linéaire de deux gradients orthogonaux, mais en réalité on prend plutôt un gradient qui se promène dans le plan pour couvrir la diffusion planaire. Il y a ensuite tout un aspect d'optimisation des waveforms qui mène à des formes de gradients funky.

## Slide 65: Diffusion: encoding
What diffusion do we measure?
How do we measure diffusion?
O
H
H
O
H
H
O
H
H
Notes: Note pour présentation physique IRM : La façon la plus simple de faire un encodage "sphérique" c'est en mettant back à back trois gradients linéaires perpendiculaires. C'est évidemment pas optimal pcq ça capture pas toutes les directions, donc on prend plutôt un gradient qui se promène dans le temps et qui encode bien la sphère. Pour le planaire, même chose, on pourrait voir ça comme la combinaison linéaire de deux gradients orthogonaux, mais en réalité on prend plutôt un gradient qui se promène dans le plan pour couvrir la diffusion planaire. Il y a ensuite tout un aspect d'optimisation des waveforms qui mène à des formes de gradients funky.

## Slide 66: Diffusion: encoding
Using dephasing and rephasing diffusion gradients.
B0
Gi
Time
Gi
First gradient
Second gradient
dephasing
Diffusion
+
++
0
+
++
0
z
y
x
0
+
++
0
0
0
0
0
+
0
0
0
0
++
0
0
0
0
After 90° RF pulse
Notes: Note pour présentation physique IRM : La façon la plus simple de faire un encodage "sphérique" c'est en mettant back à back trois gradients linéaires perpendiculaires. C'est évidemment pas optimal pcq ça capture pas toutes les directions, donc on prend plutôt un gradient qui se promène dans le temps et qui encode bien la sphère. Pour le planaire, même chose, on pourrait voir ça comme la combinaison linéaire de deux gradients orthogonaux, mais en réalité on prend plutôt un gradient qui se promène dans le plan pour couvrir la diffusion planaire. Il y a ensuite tout un aspect d'optimisation des waveforms qui mène à des formes de gradients funky.

## Slide 67: Diffusion: encoding
Stejskal and Tanner sequence (1965)
z
y
x
Gi(t)
qi(t)
t
ni
Linear
gradient
Diffusion
signal
Diffusion
propagator
"Wave"
Analogous to kx, ky and the k-space: qi and the q-space.
Notes: Note pour présentation physique IRM : La façon la plus simple de faire un encodage "sphérique" c'est en mettant back à back trois gradients linéaires perpendiculaires. C'est évidemment pas optimal pcq ça capture pas toutes les directions, donc on prend plutôt un gradient qui se promène dans le temps et qui encode bien la sphère. Pour le planaire, même chose, on pourrait voir ça comme la combinaison linéaire de deux gradients orthogonaux, mais en réalité on prend plutôt un gradient qui se promène dans le plan pour couvrir la diffusion planaire. Il y a ensuite tout un aspect d'optimisation des waveforms qui mène à des formes de gradients funky.

## Slide 68: Diffusion: sampling
Filling up the q-space
Stejskal-Tanner sequence
DSI
DTI
Single-shell HARDI
Multi-shell
HARDI
Notes: Note pour présentation physique IRM : La façon la plus simple de faire un encodage "sphérique" c'est en mettant back à back trois gradients linéaires perpendiculaires. C'est évidemment pas optimal pcq ça capture pas toutes les directions, donc on prend plutôt un gradient qui se promène dans le temps et qui encode bien la sphère. Pour le planaire, même chose, on pourrait voir ça comme la combinaison linéaire de deux gradients orthogonaux, mais en réalité on prend plutôt un gradient qui se promène dans le plan pour couvrir la diffusion planaire. Il y a ensuite tout un aspect d'optimisation des waveforms qui mène à des formes de gradients funky.

## Slide 69: Principles of MRI: sequences
Frequency encoding
Signal
Phase encoding
Slice selection
RF pulses
Pre-pulse
90° RF pulse
180° RF pulse
Gz
Gy
Gx
Spin echo
What we know so far:
90° RF pulse flips the magnetization
90 ° and 180° RF pulses create a spin echo
Pre-pulse prepares the spins for contrast
Gradients Gz select a single slice in z-axis
Gradients Gy encode the y-axis
Gradients Gx encode the x-axis and read
Gradients Gi encode the diffusion
Diffusion
encoding
Gi

## Slide 70: Diffusion: b-tensor encoding
Rules:
Water moves randomly in all directions.
Water moves around objects, not through them.
Camera: only sees water moving towards it.
Goal:
Find out what is inside the aquarium, and where.
Idea:
Taking pictures from various angles.
Time for a little game!
Regular diffusion MRI
Notes: Note pour présentation physique IRM : La façon la plus simple de faire un encodage "sphérique" c'est en mettant back à back trois gradients linéaires perpendiculaires. C'est évidemment pas optimal pcq ça capture pas toutes les directions, donc on prend plutôt un gradient qui se promène dans le temps et qui encode bien la sphère. Pour le planaire, même chose, on pourrait voir ça comme la combinaison linéaire de deux gradients orthogonaux, mais en réalité on prend plutôt un gradient qui se promène dans le plan pour couvrir la diffusion planaire. Il y a ensuite tout un aspect d'optimisation des waveforms qui mène à des formes de gradients funky.

## Slide 71: Diffusion: b-tensor encoding
Rules:
Water moves randomly in all directions.
Water moves around objects, not through them.
Camera: only sees water moving towards it and now takes a video, but at the end we only get the average picture of all the frames.
Goal:
Find out what is inside the aquarium, and where.
Idea:
Taking pictures from various angles.
Time for a little game!
B-tensor encoding diffusion MRI
Notes: Note pour présentation physique IRM : La façon la plus simple de faire un encodage "sphérique" c'est en mettant back à back trois gradients linéaires perpendiculaires. C'est évidemment pas optimal pcq ça capture pas toutes les directions, donc on prend plutôt un gradient qui se promène dans le temps et qui encode bien la sphère. Pour le planaire, même chose, on pourrait voir ça comme la combinaison linéaire de deux gradients orthogonaux, mais en réalité on prend plutôt un gradient qui se promène dans le plan pour couvrir la diffusion planaire. Il y a ensuite tout un aspect d'optimisation des waveforms qui mène à des formes de gradients funky.

## Slide 72: Diffusion: b-tensor encoding
Rules:
Water moves randomly in all directions.
Water moves around objects, not through them.
Camera: only sees water moving towards it and now takes a video, but at the end we only get the average picture of all the frames.
Goal:
Find out what is inside the aquarium, and where.
Idea:
Taking pictures from various angles.
Time for real life!
Brownian motion
Restricted diffusion
Diffusion gradient: signal drops when water is moving along its direction.
brain
Measuring signals
Notes: Note pour présentation physique IRM : La façon la plus simple de faire un encodage "sphérique" c'est en mettant back à back trois gradients linéaires perpendiculaires. C'est évidemment pas optimal pcq ça capture pas toutes les directions, donc on prend plutôt un gradient qui se promène dans le temps et qui encode bien la sphère. Pour le planaire, même chose, on pourrait voir ça comme la combinaison linéaire de deux gradients orthogonaux, mais en réalité on prend plutôt un gradient qui se promène dans le plan pour couvrir la diffusion planaire. Il y a ensuite tout un aspect d'optimisation des waveforms qui mène à des formes de gradients funky.

## Slide 73: Diffusion: b-tensor encoding
Time for real life!
z
y
x
Gi(t)
qi(t)
t
z
y
x
Gi(t)
qi(t)
t
ni
Linear gradient
Non-trivial
gradient
qi(t)
D. Topgaard, J. Magn. Reson., 2017, 275, 98-113.
q-space trajectory
b-tensor
Gi(t)
Notes: Note pour présentation physique IRM : La façon la plus simple de faire un encodage "sphérique" c'est en mettant back à back trois gradients linéaires perpendiculaires. C'est évidemment pas optimal pcq ça capture pas toutes les directions, donc on prend plutôt un gradient qui se promène dans le temps et qui encode bien la sphère. Pour le planaire, même chose, on pourrait voir ça comme la combinaison linéaire de deux gradients orthogonaux, mais en réalité on prend plutôt un gradient qui se promène dans le plan pour couvrir la diffusion planaire. Il y a ensuite tout un aspect d'optimisation des waveforms qui mène à des formes de gradients funky.

## Slide 74: Diffusion: b-tensor encoding
Using at least two encodings allows us to disentangle the isotropic and anisotropic variances.
Notes: Note pour présentation physique IRM : La façon la plus simple de faire un encodage "sphérique" c'est en mettant back à back trois gradients linéaires perpendiculaires. C'est évidemment pas optimal pcq ça capture pas toutes les directions, donc on prend plutôt un gradient qui se promène dans le temps et qui encode bien la sphère. Pour le planaire, même chose, on pourrait voir ça comme la combinaison linéaire de deux gradients orthogonaux, mais en réalité on prend plutôt un gradient qui se promène dans le plan pour couvrir la diffusion planaire. Il y a ensuite tout un aspect d'optimisation des waveforms qui mène à des formes de gradients funky.

## Slide 75: Diffusion: b-tensor encoding
Glioblastoma
Meningioma
T1
μFA
FA
T1
μFA
FA
Notes: Note pour présentation physique IRM : La façon la plus simple de faire un encodage "sphérique" c'est en mettant back à back trois gradients linéaires perpendiculaires. C'est évidemment pas optimal pcq ça capture pas toutes les directions, donc on prend plutôt un gradient qui se promène dans le temps et qui encode bien la sphère. Pour le planaire, même chose, on pourrait voir ça comme la combinaison linéaire de deux gradients orthogonaux, mais en réalité on prend plutôt un gradient qui se promène dans le plan pour couvrir la diffusion planaire. Il y a ensuite tout un aspect d'optimisation des waveforms qui mène à des formes de gradients funky.

## Slide 76: Towards understanding MRI
Physics
  Magnetic field and induction
  Spin and precession
  Magnetization
  Resonance
Principles of magnetic resonance imaging
  Signal
  Relaxation
  Sequences
Image formation
  Slice selection
  Spatial encoding
Diffusion MRI
Magnetization transfer

## Slide 77: Myelin imaging
Diffusion tensor imaging
T1 and T2 contrasts
Multiexponential T2 relaxation (MET2) imaging
Magnetization transfer
Not specific to myelin
Echo time
0
log(Signal)
Homogeneous : only
one T2 component
Heterogeneous : many
T2 components
T2 time
0
Amplitude
0
Myelin
water
Intra/extracellular
water
Myelin sheath
Axon
MWF =
+
Notes: Note pour présentation physique IRM : La façon la plus simple de faire un encodage "sphérique" c'est en mettant back à back trois gradients linéaires perpendiculaires. C'est évidemment pas optimal pcq ça capture pas toutes les directions, donc on prend plutôt un gradient qui se promène dans le temps et qui encode bien la sphère. Pour le planaire, même chose, on pourrait voir ça comme la combinaison linéaire de deux gradients orthogonaux, mais en réalité on prend plutôt un gradient qui se promène dans le plan pour couvrir la diffusion planaire. Il y a ensuite tout un aspect d'optimisation des waveforms qui mène à des formes de gradients funky.

## Slide 78: Magnetization transfer
What is it?
O
H
H
Macromolecule
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
Bound water
Free water
Bound pool
Free pool
MT pulse
Magnetization
transfer
Longitudinal magnetization
Zeeman
order
Dipolar
order
T1D
T1, bound
Zeeman
order
T1, free
RF pulse
Frequency
Bound pool
Free pool
+Δ
-Δ
Absorption lineshapes
Notes: Note pour présentation physique IRM : La façon la plus simple de faire un encodage "sphérique" c'est en mettant back à back trois gradients linéaires perpendiculaires. C'est évidemment pas optimal pcq ça capture pas toutes les directions, donc on prend plutôt un gradient qui se promène dans le temps et qui encode bien la sphère. Pour le planaire, même chose, on pourrait voir ça comme la combinaison linéaire de deux gradients orthogonaux, mais en réalité on prend plutôt un gradient qui se promène dans le plan pour couvrir la diffusion planaire. Il y a ensuite tout un aspect d'optimisation des waveforms qui mène à des formes de gradients funky.

## Slide 79: Magnetization transfer
How do we measure it?
Frequency
Bound pool
Free pool
MT pulse
+Δ
-Δ
Single RF pulse
Dual RF pulse
Zeeman and dipolar order
Zeeman order
MT
ihMT
Absorption lineshapes
Single RF pulse off-resonance.
Bound pool absorbs the energy, both Zeeman and dipolar order are in play.
Magnetization is transfered to the free pool, Mz decreases.
Not fully specific to myelin!

## Slide 80: Magnetization transfer

## Slide 81: Magnetization transfer
Inhomogeneous MT? (ihMT)
One spin ½
Pair of spins ½
Zeeman
Frequency
Energy
Single
Dual
Dual RF pulse
Single RF pulse
Regular MT
Special MT
Zeeman and dipolar
Frequency
Bound pool
Free pool
+Δ
-Δ
Absorption lineshapes
Orientation dependence
B0
n
n
Pair of spins

## Slide 82: Magnetization transfer
Inhomogeneous MT? (ihMT)
Frequency
Bound pool
Free pool
MT pulse
+Δ
-Δ
Single RF pulse
Dual RF pulse
Zeeman and dipolar order
Zeeman order
MT
ihMT
Absorption lineshapes

## Slide 83: Magnetization transfer
Inhomogeneous MT? (ihMT)
Isolates the effects of dipolar order:
  More precisely, ihMT is proportional to T1D.
  In particular, typical ihMT is sensitive to long T1D.
Lipid layers of the myelin sheaths satisfy this condition.

## Slide 84: Towards understanding MRI
Physics
  Magnetic field and induction
  Spin and precession
  Magnetization
  Resonance
Principles of magnetic resonance imaging
  Signal
  Relaxation
  Sequences
Image formation
  Slice selection
  Spatial encoding
Diffusion MRI
Magnetization transfer

## Slide 85: Image formation: slices
z
B0
Gz
RF frequency
One single
Larmor frequency
Multiple
Larmor frequencies
Magnetic field gradient
Slice thickness
Bandwidth
Gradient amplitude
Slice thickness
Bandwidth
Gradient amplitude
RF pulse

## Slide 86: Image formation: slices
z
B0
Gz
RF frequency
Spin phase
z
B0
Gz
RF frequency
Spin phase
Slice selection gradient
Spin rephasing gradient
Dephasing:
Spiral staircase
Maximum
signal

## Slide 87: Image formation: encodings
Spatial encoding with the frequency encoding gradient Gx.
Gx
+
++
0
0
0
0
0
0
0
0
0
0
0
+
++
0
+
++
0
+
++
Gx
+
++
0
0
+
++
0
+
++
0
+
++
Gx
+
++
0
0
+
++
0
+
++
0
+
++
y
x
z
Time
Notes: Tout au long de l’application du gradient G_x, le niveau de déphasage augmente (de façon périodique, en passant parfois par des rephasages). Donc durant G_x on parcourt la ligne k_x.

## Slide 88: Image formation: encodings
Gx
Gx
Phase
x
0°
360°
x
0°
360°
720°
1080°
Signal
kx
Spatial encoding of the signal from a slice, in the x-axis.
Not the FID!
Signal
Image
kx(t1)
kx(t2)
Notes: Tout au long de l’application du gradient G_x, le niveau de déphasage augmente (de façon périodique, en passant parfois par des rephasages). Donc durant G_x on parcourt la ligne k_x.

## Slide 89: Image formation: encodings
Gx
Gx
x
0°
360°
x
0°
360°
720°
1080°
S(kx(t))
kx(t)
Signal
Image
kx(t1)
kx(t3)
x
0°
360°
720°
kx(t2)
Gx
"Wave"
Dephasing
Spatial frequency
Chart: 
Chart: 
Chart: 
Notes: Tout au long de l’application du gradient G_x, le niveau de déphasage augmente (de façon périodique, en passant parfois par des rephasages). Donc durant G_x on parcourt la ligne k_x.
Corriger les formules!!!